## Slide 1: Multifamily Tool for Energy Audits (MulTEA) Training Webinar – Session 2
Mark Ternes
Mini Malhotra
Gina Accawi
Oak Ridge National Laboratory
June 15, 2017

## Slide 2: Webinar Logistics
Discussion is being recorded
Recording will be made available to all participants of this training series, especially those who miss this meeting
General protocols for web-based meetings
  Raised hands
  Chat features
  Questions to speakers/host
Will take frequent breaks during the presentations to answer questions
May mute everybody to avoid background chatter, noise, and feedback, but will unmute during breaks

## Slide 3: Agenda
Seminar 1: Tuesday, June 13
  Overview of the web-based Weatherization Assistant and MulTEA
  Agency and User forms
  Creating an Account and an Audit
  Describing a simple building in MulTEA
  Describing weatherization measures in MulTEA
Seminar 2: Thursday, June 15
  Describing more complicated buildings in MulTEA
  Entering utility bills
  Running an audit and viewing results
    Calibration run
    Individual weatherization measures run
    Package run
Seminar 3: Tuesday, June 20
  Libraries: Economic Parameters, Fuel Costs, and Measure Costs
  Final questions and discussion

## Slide 4
1
1
1
1
1
1
Enclosed Hallway
Open Hallway
1
1
1
1
Open Hallway
2
2
2
2
Describing Number of Dwelling Units by Wall Exposure
for Example Building Configurations
Box-shape building with double-loaded enclosed hallway
  Dwelling Unit Exposure-Type:
  Exposed walls in one orientation
  Exposed walls in two adjacent orientations
Box-shape building with double-loaded open hallway
  Dwelling Unit Exposure-Type:
  Exposed walls in three orientation
  Exposed walls in two opposite orientations
L-shape building with single-loaded open hallway
  Dwelling Unit Exposure-Type:
  Exposed walls in three orientation
  Exposed walls in two opposite orientations

## Slide 5
Exposed Floor
Slab on Grade Floor
Crawlspace
Below Grade Floor
Number of Floor Above Grade | 3 | 3 | 3 | 2 | 2
Number of Floors Below Grade | 0 | 0 | 0 | 1* | 1*
Elevation of First Floor Above Grade | 10 | 4 | 0 | 7 | 3
Depth of Building Below Grade | 0 | 2 | 0 | 3 | 7
* Only “partially” below grade floor may have dwelling units
Below Grade Floor
Describing the Building
for Different Foundation Types
10 ft
4+2 ft
3+7 ft
7+3 ft

## Slide 6: MulTEA’s Auditing Steps
Describe the Building
Enter Utility Bills
Calibration Run
View Calibration Results
Select Package
Package Run
View Package Results
Describe Measures
Measures Run
View Measures Results
Run 1: Calibration Run
Run 3: Package Run
Run 2: Measures Run
Modify building inputs, if needed
Modify measures details, if needed
Modify package selection, if needed

## Slide 7: Next Steps
Next webinar Tuesday, June 22 at 1:00 EDT
Recording link for this webinar and the Power Point presentation will be sent to all participants
Log in information will be sent to all participants at the end of the webinar series
  Web address
  User ID and password
    Each participant will get one set of login information
    Agency will be pre-setup for each organization
    Each person within an organization will be able to see information entered only for that organization

## Slide 8: Contacts
Mark Ternes
  865-574-0749
  ternesmp@ornl.gov
Mini Malhotra
  865-574-4317
  malhotram@ornl.gov
Gina Accawi
  865-241-9343
  accawigk@ornl.gov